Table of Contents

JUMPER & CONNECTOR LOCATION DIAGRAM	A

CHAPTER 1   INTRODUCTION	2

1-1 SYSTEM FEATURES	3

1-2 SOFTWARE POWER OFF CONTROL	4

1-3 CHECK LIST OF THE PACKING	5

CHAPTER 2   INSTALLATION	6

2-1 INSTALLATION PROCEDURES 	6

2-2 CPU INSTALLATION	7

2-3 SYSTEM MEMORY INSTALLATION	13

2-4 SRAM DESCRIPTION	14

2-5 SCSI DESCRIPTION	15

2-6 OTHER JUMPERS AND CONNECTORS 
       DESCRIPTION 	17

2-7 IDE DRIVER INSTALLATION	22

CHAPTER 3   AWARD BIOS SETUP	23

3-1 UPDATE BIOS PROCEDURES	24

3-2 AWARD SYSTEM BIOS CONFIGURATION SETUP	25

APPENDIX A 	49

CHAPTER 1  INTRODUCTION

This manual introduces how to configure the ATC-2020 mainboard for different environments. It's an overview of the layout and features of the mainboard, and also provides information for

you to change the configuration or system environment.

PART ONE includes page A and two chapters as following:

Page A contains layout diagram of the mainboard. Please refer it when you configure the system.

Chapter 1 is an overview of the mainboard features and packing

contents.

Chapter 2 describes how to upgrade and to change hardware

configurations such as memory size, CPU type, and lists of

jumper settings and connectors.

PART TWO includes chapter 3 which contains Award BIOS description..

Chapter 3 is the user's guide of AWARD BIOS setup utility, Flash ROM BIOS update procedure. The menu showed in this chapter are default settings.

Your system dealer will set up the mainboard according to your demand of computer. It means that the current settings of your mainboard's current setting may not be the same as the defaults shown in this user's manual.  If you need to change your

configuration, please ask your dealer firstly, be sure this will not

against your system warranty. Or ask for your dealer to do it for you.

REMARK

Intel  is a registered trademark of Intel Corporation.

MS-DOS is a registered trademark of Microsoft Corporation.

All other brands and product names are trademarks registered trademarks of their respective companies.

1-1 SYSTEM FEATURES

Pentium level CPU operating at 75 MHz to 200MHz with 321-pin ZIF socket 7 and scalability to accept processor in the future.

INTEL 82430HX PCIset.

Adaptec 7880 Ultra Wide SCSI Chipset.

Using four 72-pin SIM sockets, provides two banks of 64-bit wide path up to 256MB addressing page mode DRAMs.

Supporting all types of DRAM including ECC (Error Checking and Correcting) or parity, EDO (Extended Data Out), BEDO (Burst EDO), or FPM (Fast Page Mode).

Supporting four PCI bus master revision 2.1, 5V interface compliance and four 16-bit ISA slots.

Dual Master IDE connectors support up to four devices in two channels for connection of high capacity hard disk drive, CD-ROM drive, tape backup etc..

One Ultra-wide SCSI port to connect 15 devices and one Ultra SCSI port to connect 7 devices.

Supporting Dual channel USB (Universal Serial Bus) connector.

Supporting Software Power Off Control.

"True" Green power management for CPU stop clock state.

PS/2 keyboard connector and PS/2 mouse connector.

Winbond 83877 high-speed Multi-I/O chipset.

Supporting Infrared transfer (IrDA TX/RX) connection.

One FDC port supports two devices up to 2.88MB

Two 16550A fast UARTs compatiable serial ports

One EPP/ECP mode parallel port

Hardware Dimension is 305mm x 244mm (12.0" x 9.6") with four layers designed.

1-2 SOFTWARE POWER OFF CONTROL

The mainboard design supports Software Power Off Control feature through the SMM code in the BIOS under Windows 95, Windows 3.1x, and MS-DOS operation system environment. This is Intel ATX form factor feature and you should use ATX power supply.

Firstly, you should connect power switch cable (provided by ATX case supplier) to the connector “PS-ON” (next to PB SRAM chip) on the mainboard.  In the BIOS screen of ‘POWER MANAGEMENT SETUP’, choose “User Defined” (or “Min. Power Saving” or “Max. Power Saving”) in ‘Power Manager’ and choice “Yes” in ‘PM Control by APM’. (refer to page 38, 39)

In Windows 95, if you would like to power off the system, you just choose “shutdown the computer ?” in “Shut Down Windows“ from Windows 95, then the system power will be off directly, and to be stand-by status. You will find the power LED light blinking. If you would like to restart the system, just press the button of the power switch, and the system will be power on.

In Windows 3.1x or MS-DOS, you should copy the program of “down.com” (you can find it in the diskette of IDE driver) into hard drive. When you would like to power off the system, just run this “down.com”, then the system will be shutdown and stay in standby status.

Note : If you will leave your system several days, we suggest you use hardware power off to shutdown your system.

1-3 CHECK LIST OF THE PACKING

The mainboard comes securely packed in a durable box and shipping carton. If any of the above items are missing or damaged, please contact your supplier.

Each mainboard containing:

Q'TY     	Description

1                 Mainboard 	: ATC-2020.

1	Diskette	: Enhanced IDE driver (3.5").

3	Diskette	: SCSI driver (3.5").

1                	Cable 	: Enhanced IDE connector.

1               	Cable 	: F.D.D. connector.

1	Cable 	: Ultra SCSI port.

1               	Cable 	: Ultra-wide SCSI port. (option)

1             	Manual 	: ATC-2020 User`s manual.

1             	Manual 	: Adaptec SCSI User`s manual.

NOTE : Leave the mainboard in its original packing until you are ready to install it.

CHAPTER 2  INSTALLATION

2-1 INSTALLATION PROCEDURE

Before installing the computer, please prepare all components such as CPU, DRAM; peripherals such as hard disk drive, keyboard, CD-ROM drive; and accessories such as cables. Then, install the system as following .

1. Plug CPU (with heat sink and cooling fan), DRAM modules in

the mainboard.

2. Set jumpers based on your configuration.

3. Plug add-on cards in PCI or ISA slots.

4. Connect cables to peripherals, power supply..

5. Make sure all components and devices are well connected,

turn on the power and setup System BIOS based on your

configuration.

6. Install peripheral, add-on card drivers and test them.

7. If all of above procedures are success, turn-off the power then

plug all of them into your computer case.

2-2 CPU  INSTALLATION

ATC-2020 supports Pentium level CPU up to 200MHz. For installation, please notice CPU pin 1 must align with the ZIF socket 7 Pin 1 location. Before you install or upgrade your CPU, please read CPU guide from CPU manufacturer to make sure the CPU voltage specification. Then choice the right installation in the 2-2-1 based on your CPU type/brand and follow the description to setup jumpers. If your CPU is not in the list of 2-2-1, please refer to 2-2-2 and 2-2-3 for installation.

2-2-1 CPU TYPE SELECTION

A. INTEL PENTIUM CPU (P54C)

| JP3 |  | 1-2 |  |
| --- | --- | --- | --- |

| CPU Core Voltage | VRE | STD |  | JP5 | 1-2** | 3-4* |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| INTERNAL CPU CLOCK | JP8 | JP9 | JP10 | JP6 | JP7 | Ext.x Frq. |  | 75MHz | close | close | open | 1-2 | 1-2 | 50x1.5 |  | 90MHz | close | open | open | 1-2 | 1-2 | 60x1.5 |  | 100MHz | open | close | open | 1-2 | 1-2 | 66x1.5 |  | 120MHz | close | open | open | 2-3 | 1-2 | 60x2.0 |  | 133MHz | open | close | open | 2-3 | 1-2 | 66x2.0 |  | 150MHz | close | open | open | 2-3 | 2-3 | 60x2.5 |  | 166MHz | open | close | open | 2-3 | 2-3 | 66x2.5 |  | 180MHz | close | open | open | 1-2 | 2-3 | 60x3.0 |  | 200MHz | open | close | open | 1-2 | 2-3 | 66x3.0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

B. INTEL PENTIUM CPU (MMX P55C)

| JP3 |  | 2-3 |  |
| --- | --- | --- | --- |

| CPU Core Voltage | 3.5V | 3.3V | 2.9V | 2.8V* | 2.7V |  | JP5 | 1-2 | 3-4 | 5-6 | 7-8 | 9-10 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

*Currently, Intel P55C is released 2.8V core voltage only.  Please confirm this with your system supplier before you install P55C CPU.

| INTERNAL CPU CLOCK | JP8 | JP9 | JP10 | JP6 | JP7 | Ext.x Frq. |  | 166MHz | open | close | open | 2-3 | 2-3 | 66x2.5 |  | 180MHz | close | open | open | 1-2 | 2-3 | 60x3.0 |  | 200MHz | open | close | open | 1-2 | 2-3 | 66x3.0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

C. Cyrix 6x86 CPU

| JP3 | JP5 |  | 1-2 | 1-2 |  |
| --- | --- | --- | --- | --- | --- |

| INTERNAL CPU CLOCK | JP8 | JP9 | JP10 | JP6 | JP7 | Ext.x Frq. |  | P120+ @ 100MHz | close | close | open | 2-3 | 1-2 | 50x2.0 |  | P133+ @ 110MHz | open | open | open | 2-3 | 1-2 | 55x2.0 |  | P150+ @ 120MHz | close | open | open | 2-3 | 1-2 | 60x2.0 |  | P166+ @ 133MHz | open | close | open | 2-3 | 1-2 | 66x2.0 |  | P200+ @ 150MHz | close | open | close | 2-3 | 1-2 | 75x2.0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

D. AMD K5 CPU

| JP3 | JP5 |  | 1-2 | 1-2 |  |
| --- | --- | --- | --- | --- | --- |

| INTERNAL CPU CLOCK | JP8 | JP9 | JP10 | JP6 | JP7 | Ext.x Frq. |  | PR75ABR 75MHz | close | close | open | 1-2 | 1-2 | 50x1.5 |  | PR90ABQ 90MHz | close | open | open | 1-2 | 1-2 | 60x1.5 |  | PR100ABQ 100MHz | open | close | open | 1-2 | 1-2 | 66x1.5 |  | PR120ABQ 90MHz | close | open | open | 1-2 | 1-2 | 60x1.5 |  | PR133ABQ 100MHz | open | close | open | 1-2 | 1-2 | 66x1.5 |  | PR166ABQ | open | close | open | 2-3 | 2-3 | 66x1.75 |  | PR200ABQ 133MHz | open | close | open | 2-3 | 1-2 | 66x2.0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2-2-2 CPU VOLTAGE SETTING

JP3 is for setting single or dual CPU voltage mode. JP5 is used for various CPU voltage value types, please refer to CPU‘s marking on/under CPU and its user’s manual.

| CPU MODE | Single | Dual |  |
| --- | --- | --- | --- |

JP3

1-2

| 2-3 |  |
| --- | --- |

| CPU CORE VOLTAGE | JP5 |  | INTEL | STD | 3-4 |  | (P54C) | VRE | 1-2 |  | P55C | 2.8V* | 7-8 |  | Cyrix | 6x86(028) | 1-2 |  | AMD | K5 | 1-2 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2-2-3 CPU CLOCK SETTING

The following setting is for new CPU speed released.

| EXTERNAL CPU CLOCK | JP8 | JP9 | JP10 |  | 50(MHz) | close | close | open |  | 55(MHz) | open | open | open |  | 60(MHz) | close | open | open |  | 66(MHz) | open | close | open |  | 75(MHz) | close | open | close |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

External

CPU Clock :

| INTERNAL CPU CLOCK | JP6 | JP7 |  | INTEL EXTERNAL CLOCK X 1.5 | 1-2 | 1-2 |  | INTEL EXTERNAL CLOCK X 2.0 | 2-3 | 1-2 |  | INTEL EXTERNAL CLOCK X 2.5 | 2-3 | 2-3 |  | INTEL EXTERNAL CLOCK X 3.0 | 1-2 | 2-3 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Internal

CPU Clock :

2-3 SYSTEM MEMORY INSTALLATION

ATC-2020 provides four 72-pin SIM sockets for system memory expansion from 4MB to 256MB. These four SIMs are arranged to two banks, Bank0 (SIM 1, 2) and  Bank1(SIM 3, 4), please refer to page A. Each bank provides 64-bit wide data path.

The mainboard accepts Fast Page Mode DRAM, and EDO Mode (Extended Data Out) DRAM, with a speed at least 70 nanosecond. You should plug DRAM modules into two sockets (same bank) or four sockets at one time. Each pair of modules must be the same size, type, and speed; no matter single-side or double-side module. Please plug in Bank 0 firstly if you only have 2 modules. The mainboard supports mixing of EDO DRAM SIMMs with fast page

mode DRAM SIMMs among different banks; please plug EDO in Bank 0, if you only have 2 EDO modules.

If you install more than 64MB DRAM on ATC-2020, and would like to get more than 64MB cacheable size function, you should plug one 16K8 (or 32K8) TAG RAM into U22 socket, and change BIOS value of ‘L2 Cache Cacheable Size’ to ‘512MB’. ( refer to the screen of “CMOS SETUP UTILITY”.; page 32)

°¡ System Memory Combinations Options °¡

| BANK0 | BANK1 | Total Memory |  | SIM 1, 2 | SIM 3, 4 | SIM 1- 4 |  | 2MBx2 | - | 4MB |  | - | 2MBx2 | 4MB |  | 4MBx2 | - | 8MB |  | - | 4MBx2 | 8MB |  | 8MBx2 | - | 16MB |  | - | 8MBx2 | 16MB |  | 4MBx2 | 4MBx2 | 16MB |  | 4MBx2 | 8MBx2 | 24MB |  |  | - continue - |  |  | 8MBx2 | 4MBx2 | 24MB |  | 16MBx2 | - | 32MB |  | - | 16MBx2 | 32MB |  | 8MBx2 | 8MBx2 | 32MB |  | 4MBx2 | 16MBx2 | 40MB |  | 16MBx2 | 4MBx2 | 40MB |  | 8MBx2 | 16MBx2 | 48MB |  | 16MBx2 | 8MBx2 | 48MB |  | 32MBx2 | - | 64MB |  | - | 32MBx2 | 64MB |  | 16MBx2 | 16MBx2 | 64MB |  | 4MBx2 | 32MBx2 | 72MB |  | 32MBx2 | 4MBx2 | 72MB |  | 8MBx2 | 32MBx2 | 80MB |  | 32MBx2 | 8MBx2 | 80MB |  | 16MBx2 | 32MBx2 | 96MB |  | 32MBx2 | 16MBx2 | 96MB |  | 64MBx2 | - | 128MB |  | - | 64MBx2 | 128MB |  | 32MBx2 | 32MBx2 | 128MB |  | 4MBx2 | 64MBx2 | 136MB |  | 64MBx2 | 4MBx2 | 136MB |  | 8MBx2 | 64MBx2 | 144MB |  | 64MBx2 | 8MBx2 | 144MB |  | 16MBx2 | 64MBx2 | 160MB |  | 64MBx2 | 16MBx2 | 160MB |  | 32MBx2 | 64MBx2 | 192MB |  | 64MBx2 | 32MBx2 | 192MB |  | 64MBx2 | 64MBx2 | 256MB |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2-4 SRAM  DESCRIPTION

ATC-2020 is built-in 256KB or 512KB Sync. Pipeline Burst SRAM on board.

SRAM SIZE

PB SRAM

(U19, U20)

TAG SRAM

| (U21) |  | 256KB | 32K32 x 2pcs | 16K8 x 1pc or |  | 512KB | 64K32 x 2pcs | 32K8 x 1pc |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

U22 TAG SRAM chip socket is used for getting more than 64MB cacheable size fuction. (more than 64MB DRAM required). You should change BIOS value of ‘L2 Cache Cacheable Size’ to ‘512MB’ also. ( refer to the screen of “CMOS SETUP UTILITY”.; page 32)

2-5 SCSI DESCRIPTION

ATC-2020 supports SCSI interface including one Ultra-wide SCSI and one Ultra SCSI. You can use both of them in the same time. The Ultra-wide SCSI port can connect maximum 15 devices, and the Ultra SCSI port can connect maximum 7 devices. The system maximum can connect 15 devices whether you use one or two SCSI ports.

For installation of SCSI peripherals, you should install SCSI driver and adjust BIOS value of ‘Onboard PCI SCSI chip’ to “Enable”. ( refer to the screen of “PNP/PCI CONFIGURATION ”.; page 32)

For more SCSI peripherals installation information please refer to Adaptec user manual named -- Adaptec 7800 Family Manager Set for Netware, OS/2, Windows 95, Windows NT, SCO UNIX, and UnixWare. The part number is : 510896-00

°¡JP11 is set for SCSI Multiple Computer Termination.

| open | Nomal |  | close | Multiple Computer Termination |  |
| --- | --- | --- | --- | --- | --- |

°¡JP14 is SCSI LED indicator.

2-6 OTHER JUMPERS AND

CONNECTORS  DESCRIPTION

Please refer to page A for the location of the following jumpers.

| Jumper | Function | Remark |  | JP13 | CMOS |
| --- | --- | --- | --- | --- | --- |

open: Normal¯¡

| close: Clear CMOS |  |
| --- | --- |

¯¡is default setting

The locations of following connectors are indicated in page A.

When you plug a cable into the following I/O connectors, you should have the pin 1 edge of the cable aligned with the pin 1 end of the connector.

CN8 : Speaker, Keyboard Lock, Reset, SMI,

Turbo LED, and IDE LED connectors.

JP1 : CPU cooling fan connector. Wire with +12V

voltage (most likely red wire) must be plugged

into pin2, and GROUND wires (most likely

black wires) must be plugged into pin1 and/or

pin3. please confirm the wire color represen-

tation with your supplier.

CAUTION: Plug wire into wrong connector will

DAMAGE fan and mainboard.

IR1 : Infrared module connector.

USB : Universal Serial Bus connector, this is

used to connect USB devices through an

optional dual head cable with a iron plane.

CN1 : PS/2 style compatible keyboard

connector. (signal same as CN2)

CN2 : PS/2 mouse connector, which is used to

connect an optional cable.

pin1 : data

pin2 : N/C

pin3 : GND

pin4 : VCC

pin5 : clock

pin6 : N/C

PW2 : AT mode +5V power supply connector.

PW1 : ATX mode +3.3/5/12V power supply

connector.

1                       10

11                        20

COM1/2 : this two connectors are used to

connect serial port cables.

| pin | signal name |  | 1 | DCD |  | 2 | Serial In |  | 3 | Serial Out |  | 4 | DTR |  | 5 | GND |  | 6 | DSR |  | 7 | RTS |  | 8 | CTS |  | 9 | RI |  | 10 | N/C |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

FDC1 : this connector is used to connect floppy

disk drive through cable.

| pin | signal | pin | signal |  | 2 | RWC- | 20 | STEP- |  | 4 | reserved | 22 | Write Data |  | 6 | FDEDIN | 24 | Write Gate |  | 8 | Index- | 26 | Track 00- |  | 10 | Motor EnableA- | 28 | Write Protect- |  | 12 | Drive Sele.B- | 30 | Read Data- |  | 14 | Drive Sele.A- | 32 | Side 1 Sele.- |  | 16 | Motor EnableB- | 34 | DisketteChange |  | 18 | DIR- |  |  |  | All of odd pins are ground |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

LPT1

LPT1 : this connector is used to connect parallel

port cable.

| pin | signal | pin | signal |  | 1 | STROBE- | 10 | ACK- |  | 2 | Data Bit 0 | 11 | BUSY |  | 3 | Data Bit 1 | 12 | PE |  | 4 | Data Bit 2 | 13 | SLCT |  | 5 | Data Bit 3 | 14 | Auto Feed- |  | 6 | Data Bit 4 | 15 | ERROR- |  | 7 | Data Bit 5 | 16 | INIT- |  | 8 | Data Bit 6 | 17 | SLCT IN- |  | 9 | Data Bit 7 | 26 | N/C |  | pin18 -- pin25 are ground |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

IDE1/2 : these two connectors are used to connect

IDE devices through IDE cables, total 4 devices.

| pin | signal | pin | signal |  | 1 | Reset IDE | 21 | DDRQ0(1) |  | 2 | GND | 22 | GND |  | 3 | Host Data 7 | 23 | I/O Write- |  | 4 | Host Data 8 | 24 | GND |  | 5 | Host Data 6 | 25 | I/O Read- |  | 6 | Host Data 9 | 26 | GND |  | 7 | Host Data 5 | 27 | IORDY |  | 8 | Host Data 10 | 28 | N/C |  | 9 | Host Data 4 | 29 | DDAK0-(1)- |  | 10 | Host Data 11 | 30 | GND |  | 11 | Host Data 3 | 31 | IRQ14* |  | 12 | Host Data 12 | 32 | IOCS16- |  | 13 | Host Data 2 | 33 | Addr 1 |  | 14 | Host Data 13 | 34 | N/C |  | 15 | Host Data 1 | 35 | Addr 0 |  | 16 | Host Data 14 | 36 | Addr 2 |  | 17 | Host Data 0 | 37 | Chip Sele.1P- |  | 18 | Host Data 15 | 38 | Chip Sele 3P- |  | 19 | GND | 39 | Activity |  | 20 | Key | 40 | GND |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2-7 IDE DRIVER INSTALLATION

Setup for DOS/Windows :

1. Starting MS-Windows 3.1 (or 3.11)

2. Select Program Manager, "RUN" a file, then type "A:\setup.exe"

3. Exit MS-Windows, turn power off; then turn power on.

Setup for Windows 95 :

1. Starting Windows 95

2. Select “My Computer”; select “Control Panel”; select “System”;

then select “Device Manager”, “Hard Disk Controllers”.

3. Double-click to remove default driver program, restart computer.

4. Follow the instructions on your screen to install new IDE driver

we offer in the 3.5“ diskette

5. Exit Windows 95, turn power off; then turn power on.

°¡For more information, please refer to Windows 95 manual.

Make sure your HDD should follow ATA standard, and your CD-ROM drive should follow ATAPI standard. When you plug-in the IDE devices, please plug your first and second devices into IDE 1 port (Master then Slave), then plug third and forth devices into IDE 2 port. If you have CD-ROM drive, please set it behind hard disk devices as the last device. For example, if you have 2 HDDs and 1 CD-ROM drive, you should set HDD1 and HDD2 in IDE1 Master and Slave, set CD-ROM drive in IDE 2 Master. Master and Slave, set CD-ROM drive in IDE 2 Master. Some brands of the device combination may not work under this sequence, you can try to re-arrange the devices sequence and retry to run it, or contact your vendor. Following table is the recommend sequence.

CHAPTER 3  AWARD BIOS

SETUP

This chapter explains the system BIOS setup, and how to update new BIOS. All BIOS screens showed in the following pages are default values, your system dealer will set up these values according to your demand of computer.

ATC-2020 uses Flash ROM to make BIOS easier to be updated by the floppy disk-based program. and to committe Microsoft

Windows 95 plug & play feature.

°¡  JP13 Setting is for Update System BIOS

| open | NORMAL¯¡ |  | close | CLEAR CMOS |  |
| --- | --- | --- | --- | --- | --- |

¯¡is default setting

NOTE : If your mainboard is used

‘Benchmarq‘ battery, you

should clear CMOS under

powering on, otherwise the

‘clear’ will not work.

°¡  JP12 Setting is for Voltage of Flash ROM

| 1-2 | +5V |  | 2-3 | +12V |  |
| --- | --- | --- | --- | --- | --- |

3-1 UPDATE BIOS PROCEDURES

If the BIOS needs to be updated, it can be obtained on a diskette from your system supplier. The BIOS diskette includes 3 files:

“awdflash.exe”  --  BIOS update utility program

“readme.txt”

“(update BIOS filename with version number).rom”

The update procedures are as following:

Boot the system to DOS mode in a normal manner.

Insert the updated diskette to drive A (or B).

Change working directory to floppy drive, A or B, which contains the update BIOS diskette. --  Type “a:\” or “b:\”, “ENTER”.

Run the BIOS update utility  --  Type “awdflash”, “ENTER”.

Type “(update BIOS file name with version number).rom”, ENTER.

Type “N” when the screen displays the message : " Do you want to save BIOS (Y/N) ?".

Type “Y“ when the screen shows the message : " Are you sure to  program (Y/N) ?".

Follow instructions displayed on the screen.  DO NOT remove the update BIOS diskette from the floppy drive nor turn the system power off until the BIOS update is completed.

Exit the utility and turn the system power off, set JP12 to 'close' to clear the CMOS. After about 10 seconds, set JP12 to 'open' (remove the jumper cap ), become the normal status.

Turn the system power on and test your system working properly or not.

3-2  AWARD SYSTEM BIOS

CONFIGURATION SETUP

The following pages explain how to set up the system configuration (CMOS) under the AWARD BIOS. The SETUP program is stored in the Read-Only-Memory (ROM) on the mainboard. To do the SETUP procedure, press the <Del> key when the system is booting up. The following main menu will appear. Please select " STANDARD CMOS SETUP" to enter the next screen.

ROM PCI/ISA BIOS (2A59FA29)

CMOS SETUP UTILITY

AWARD SOFTWARE, INC.

| STANDARD CMOS SETUP | INTEGRATED PERIPHERALS |  | BIOS FEATURES SETUP | PASSWORD SETTING |  | CHIPSET FEATURES SETUP | IDE HDD AUTO DETECTION |  | POWER MANAGEMENT SETUP | SAVE & EXIT SETUP |  | PNP/PCI CONFIGURATION | EXIT WITHOUT SAVING |  | LOAD BIOS DEFAULTS |  |  | LOAD SETUP DEFAULTS |  |  | ESC: Quit | :Select Item |  | F10: Save & Exit Setup | (Shift) F2 : Change Color |  | Time, Date, Hard Disk Type ..... |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The section on the bottom of the main menu explains how to control this screen.  The other one section displays the items highlighted in the list.

This screen records some basic hardware information, and set the system clock and error handling. These records can be lost or corrupted if the on-board battery  is failed or  weak.

ROM PCI/ISA BIOS (2A59FA29)

CMOS SETUP UTILITY

AWARD SOFTWARE, INC.

| STANDARD CMOS SETUP | INTEGRATED PERIPHERALS |  | BIOS FEATURES SETUP | PASSWORD SETTING |  | CHIPSET FEATURES SETUP | IDE HDD AUTO DETECTION |  | POWER MANAGEMENT SETUP | SAVE & EXIT SETUP |  | PNP/PCI CONFIGURATION | EXIT WITHOUT SAVING |  | LOAD BIOS DEFAULTS |  |  | LOAD SETUP DEFAULTS |  |  | ESC: Quit | :Select Item |  | F10: Save & Exit Setup | (Shift) F2 : Change Color |  | Time, Date, Hard Disk Type ..... |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

ROM PCI/ISA BIOS (2A59FA29)

STANDARD CMOS SETUP

AWARD SOFTWARE, INC.

| Date (mm:dd:yy) : Fri, Jun 14 1996 |  |  | Time(hh:mm:ss) : 13 : 37 : 14 |  |  | HARD DISKS TYPE SIZE CYLS HEAD PRECOMP LANDZ SECTOR MODE |  | Primary Master : Auto 0 0 0 0 0 0 Auto |  | Primary Slave : None 0 0 0 0 0 0 ---- |  | Secondary Master : None 0 0 0 0 0 0 ----- |  | Secondary Slave : None 0 0 0 0 0 0 ---- |  |  |  |  | Drive A : 1.44M, 3.5 in. | Base Memory : 640K |  | Drive B : None | Extended memory : 7168K |  |  | Other Memory : 384K |  | Video : EGA/VGA | ------------------------------------------------ |  | Halt On: All Errors | Total Memory : 8192K |  | ESC : Quit :Select Item PU/PD/+/- : Modify |  | F1 : Help (Shift) F2 : Change Color |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Date	mm is month, dd is date, yy is year.

| date | from 1 to 31 |  | month | from Jan. to Dec. |  | year | from 1900 to 2099 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Time	hh is hour, mm is minute, ss is second.

| hh | from 0 to 23 (24-hour military -time) |  | mm | from 0 to 59 |  | ss | from 0 to 59 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Primary Master	These categories identify the types of 2 channels

Primary Slave	that have been installed in the computer. There

Secondary Master	are 45 predefined types and 4 user definable

Secondary Slave	types are for Enhanced IDE BIOS. Type 1 to 45

are predefined. Type ‘user’ is user-definable.

Press PgUp/PgDn to select a numbered hard

disk type or type the number and press<Enter>.

If you select ‘Auto’ BIOS will auto-detect the

HDD & CD-ROM Drive at the POST stage and

showing the IDE for HDD & CD-ROM Drive. If

you select ‘user’, you will need to know the

information listed below. Enter the information 		directly from the keyboard and press <Enter>. 		This information should be from your hard disk

vender or dealer. If the controller of HDD

interface is ESDI, the selection shall be ‘Type			1’; is SCSI, the selection shall be ‘None’.

If the device has not been installed select

‘NONE’ and press <Enter>.

| Type | drive type |  | SIZE | automatically adjusts |  | CYLS | number of cylinders |  | HEAD | number of heads |  | PRECOMP | write precom |  | LANDZ | landing zone |  | SECTOR | number of sectors |  | MODE | mode type |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Drive A	This category identifies the types of floppy disk

Drive B	drive A or drive B that have been installed in 			the computer.

| None | No floppy drive installed |  | 360K, 5.25 in | 5.25“ PC-type 360KB capacity |  | 1.2M, 5.25 in | 5.25“ AT-type 1.2MB capacity |  | 720K, 3.5 in | 3.5“ double-side 720KB capacity |  | 1.44M, 3.5 in | 3.5“ double-side 1.44MB capacity |  | 2.88M, 3.5 in | 3.5“ double-side 2.88MB capacity |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Video	This category selects the type of video adapter

used for the primary system monitor. Although

secondary monitors are supported, you do not

have to select the type in Setup.

Halt On	This category determines whether the computer

will stop if an error is detectd during power up.

| No errors | When the BIOS detects a non-fatal error the system will be stopped and you will be prompted |  | All errors | The system boot will not be stopped for any error that may be detected |  |
| --- | --- | --- | --- | --- | --- |

All, But

| Keyboard | The system boot will not stop for a keyboard error, it will stop for all other errors |  |
| --- | --- | --- |

All, But

Diskette

The system boot will not stop for a disk error, it will stop for all other errors

All, But

| Disk/Key | The system boot will not stop for a disk or keyboard error, it will stop for all other errors |  |
| --- | --- | --- |

Memory	This category is display-only which is determined

by POST (Power On Self Test) of the BIOS.

Base Memory  The value of the base memory

is typically 512K or 640K based on the memory

installed on the mainboard.

Extended Memory  How much extended

memory is present during the POST. This is

the amount of memory located above 1MB in

the CPU‘s memory address map.

Other Memory  This refers to the memory

located in the 640K to 1024K address space.

The BIOS is the most frequent user of this RAM

area since this is where it shadows RAM.

This screen is a list of system configuration options. Some of them are defaults required by the mainboard's design, others depend on the features of your  system.

ROM PCI/ISA BIOS (2A59FA29)

CMOS SETUP UTILITY

AWARD SOFTWA

# Text boxes

C.

| STANDARD CMOS SETUP | INTEGRATED PERIPHERALS |  | BIOS FEATURES SETUP | PASSWORD SETTING |  | CHIPSET FEATURES SETUP | IDE HDD AUTO DETECTION |  | POWER MANAGEMENT SETUP | SAVE & EXIT SETUP |  | PNP/PCI CONFIGURATION | EXIT WITHOUT SAVING |  | LOAD BIOS DEFAULTS |  |  | LOAD SETUP DEFAULTS |  |  | ESC: Quit | :Select Item |  | F10: Save & Exit Setup | (Shift) F2 : Change Color |  | Virus, Protection, Boot Sequence |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

ROM PCI/ISA BIOS (2A59FA29)

BIOS FEATURES SETUP

AWARD SOFTWARE, INC.

| Virus Warning | : Disabled | Video BIOS Shadow | : Enabled |  | CPU Internal Cache | : Enabled | C8000-CBFFF Shadow | : Disabled |  | External Cache | : Enabled | CC000-CFFFF Shadow | : Disabled |  | Quick Power On Self Test | : Disabled | D0000-D3FFF Shadow | : Disabled |  | Boot Sequence | : A,C,SCSI | D4000-D7FFF Shadow | : Disabled |  | Swap Floppy Drive | : Disabled | D8000-DBFFF Shadow | : Disabled |  | Boot Up Floppy Seek | : Enabled | DC000-DFFFF Shadow | : Disabled |  | Boot Up NumLock Status | : On |  |  |  | Boot Up System Speed | : High |  |  |  | Gate A20 Option | : Normal |  |  |  | Typematic Rate Setting | : Disabled |  |  | Typematic Rate(Chars/Sec) | : 6 | Esc : Quit :Select Item |  | Typematic Delay(Msec) | : 250 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

F1   : Help